## Slide 1: The Spirits of Web of Things Past, Present, and Yet to Come
Matthias Kovatsch, Summer School on AI for Industry 4.0, 27 Jul 2020

## Slide 2: Dr. Matthias Kovatsch Principal Researcher
Education
2003 – 2008 Dipl.-Ing., FAU Erlangen-Nürnberg, Germany
2009 – 2014 Dr. sc., ETH Zurich, Switzerland
Work Experience
2006 – 2009 Working Student, Fraunhofer IIS, Germany
2011 ~ 2015 Visiting Researcher, RISE SICS, Sweden (multiple visits)
2014 – 2015 Visiting Researcher, Samsung Electronics, South Korea
2016 – 2018 Senior Research Scientist, Siemens AG, Germany
2019 – now Principal Researcher, Huawei Technologies, Germany
Roles
Eclipse IoT Working Group Member (inactive)
IETF IoT Directorate Member
W3C Web of Things Interest Group & Working Group Co-Chair (inactive)
OPC Foundation Field Level Communication Initiative Steering Committee Member
Projects
Eclipse Thingweb (node-wot)
Eclipse Californium
Contiki Erbium
Firefox Copper (deprecated)

## Slide 3: The Spirits of Web of Things
Past
Web Presences
Putting Things to REST
Constrained RESTful Environments
Yet to Come
More Bindings
More Semantics
Better Actions
Present
W3C Standardization
Thing Description
node-wot

## Slide 4: The Spirits of Web of Things
Past
Web Presences
Putting Things to REST
Constrained RESTful Environments
Yet to Come
More Bindings
More Semantics
Better Actions
Present
W3C Standardization
Thing Description
node-wot

## Slide 5: A Little History
2002
Web
Presences
People, Places, Things
“Cooltown”
IoT
1999
RFID
Virtual
Representations
Internet of Things
UbiComp
QR Codes
Connecting the physical world
with the virtual world

## Slide 6: Web Presences for People, Places, Things
WoT Ideas from 2002 ... 2006
Physical Web: URIs via BLE beacon
Kindberg et al. “People, places, things: Web presence for the real world.” Mobile Networks and Applications 7(5):365-76. Oct 2002
Rukzio et al. “Mobile Service Interaction with the Web of Things.” Proc. ICT 2006, Funchal, Madeira Island, Portugal, May 2006

## Slide 7: A Little History
Web of Things
2007
Usability Interoperability
2002
Web
Presences
People, Places, Things
“Cooltown”
IoT
1999
RFID
Virtual
Representations
UbiComp
Connected Devices
2003
TinyOS
Contiki
QR Codes
Wireless Sensor Networks
2001
“Smart Dust”
Connecting the physical world
with the virtual world

## Slide 8: Putting Things to REST – Towards WoT
Use Representational State Transfer, the architectural style of the Web, to communicate with Things
Web resources allow loose coupling between devices and applications
HTTP enables interoperability and libraries available for most platforms
Wilde. Putting Things to REST. UCB iSchool Report 2007-015. Nov 2007
Guinard,Trifa. Building the Web of Things. Manning Publications. Jun 2016

## Slide 9: A Little History
Web of Things
2007
Usability Interoperability
2002
Web
Presences
People, Places, Things
“Cooltown”
IoT
1999
RFID
6LoWPAN
Virtual
Representations
UbiComp
Connected Devices
2003
IP-based IoT
TinyOS
Contiki
QR Codes
Wireless Sensor Networks
“Smart Dust”
2008
Constrained RESTful Environments
2010
Gateways
Web server with lots of adaptation code

## Slide 10: Constrained Application Protocol (CoAP)
New Web protocol for low-power networks and resource-constrained devices
Designed from scratch following the REST architectural style
Transparent mapping to HTTP
Additional features for IoT applications
CoAP servers
directly on
devices
Message Sub-layer
Reliability
UDP
DTLS
TLS
Request-Response Sub-layer
RESTful interaction
CoAP
WSS
…
Shelby, Hartke, Bormann. “The Constrained Application Protocol (CoAP).” RFC 7252. Jun 2014

## Slide 11: Why the Web?
Internet of Things
  Domain expertise
  Embedded developers
  Optimized protocols and formats
    Silos with high integration costs
World Wide Web
  Interoperability and usability
  Web developers
  HTTP, JSON, scripting
    Application mashups
Web of Things
  Take patterns that worked for the Web
  Adapt and apply them to the IoT
Profiles 4,450,002
Profiles 336,951
Notes: Add figure of developer profiles (80-20 story)
Hotels mashup

## Slide 12: But this an AI Summer School?!

## Slide 13: Spirit of the Past: Digitalization
All these technologies form the foundation to enable AI
  Connected devices are required to collect the data for data-driven machine learning
  Proper protocols and APIs are required to enable automated control and optimization
  Developers are provided to carry out the digitalization at scale
Digitalization allows to monitor and quantify processes in real-time
“Industry 4.0” describes the digitalization of industries

## Slide 14: The Spirits of Web of Things
Past
Web Presences
Putting Things to REST
Constrained RESTful Environments
Yet to Come
More Bindings
More Semantics
Better Actions
Present
W3C Standardization
Thing Description
node-wot

## Slide 15: W3C Standardization Activity
W3C WoT Community Group (CG) No charter needed
Started summer 2013
~300 participants
Free discussion (no membership needed)
W3C WoT Workshop, Berlin, 2014
Identify stakeholders for standards work
Believe in benefits of Web technology for IoT
Web standards are horizontal and neutral

## Slide 16: W3C Standardization Activity
W3C WoT Interest Group (IG) https://w3c.github.io/wot/charters/wot-ig-2019.html
Started spring 2015
~200 participants
Informal work, outreach
Exploration of new building blocks
“PlugFests” validation with running code
“OpenDays” with also external speakers
Liaisons and collaborations with other organizations and SDOs
W3C WoT Working Group (WG) https://www.w3.org/2020/01/wot-wg-charter.html
Started end of 2016
~100 participants
Normative work
Work on deliverables
W3C Patent Policy for royalty-free standards
Only W3C Members and Invited Experts

## Slide 17: Describe Existing IoT Ecosystems
Any IoT Device
SDK
Application
Data Model
Protocol
Form an implicit interaction model,
which is usually not well documented
The IoT has a plethora of protocols,
often dialects due to custom options for protocols such as HTTP, CoAP, MQTT, etc.
Provide semantic metadata that uniformly describes how to interact with Things
Capture each protocol once in a uniform template that describes how to configure protocol stacks (e.g., CoAP or MQTT) to send the message expected by the Thing
Every SDK and library is different,
so that application development is expensive
Define a common runtime similar to the Web browser
to implement Thing behavior

## Slide 18: Describe Existing IoT Ecosystems
Events
Properties
Actions
“Interaction Affordances”
Any IoT Device
SDK
Application
Protocol
The IoT has a plethora of protocols,
often dialects due to custom options
Capture each protocol once in a uniform template that describes how to configure protocol stacks (e.g., CoAP or MQTT) to send the message expected by the Thing
Interaction Model
An index.html
for Things
JSON-LD representation format to describe Thing instances with metadata. Uses formal interaction model and domain-specific vocabularies to uniformly describe Things, their capabilities, and how to use them.
WoT Thing Description (TD)
TD
Every SDK and library is different,
so that application development is expensive
Define a common runtime similar to the Web browser
to implement Thing behavior

## Slide 19: Affordances
“Affordance refers to the perceived and actual properties of the thing, primarily those fundamental properties that determine just how the thing could possibly be used.” – Donald Norman on everyday things
“… the simultaneous presentation of information and controls such that the information becomes the affordance through which the user obtains choices and selects actions.” – Roy Fielding on hypermedia
(Web Links and Forms)
Handle = Affordance
What?
How?
Open
Crank
Twist
= Information + Control
Door = Thing
(Property, Action, Event)
Push

## Slide 20: Describe Existing IoT Ecosystems
Events
Properties
Actions
“Interaction Affordances”
Any IoT Device
SDK
Application
Protocol
The IoT has a plethora of protocols,
often dialects due to custom options
Capture each protocol once in a uniform template that describes how to configure protocol stacks (e.g., CoAP or MQTT) to send the message expected by the Thing
Interaction Model
An index.html
for Things
JSON-LD representation format to describe Thing instances with metadata. Uses formal interaction model and domain-specific vocabularies to uniformly describe Things, their capabilities, and how to use them.
WoT Thing Description (TD)
TD
Every SDK and library is different,
so that application development is expensive
Define a common runtime similar to the Web browser
to implement Thing behavior

## Slide 21: Describe Existing IoT Ecosystems
Any IoT Device
SDK
Application
Every SDK and library is different,
so that application development is expensive
Define a common runtime similar to the Web browser
to implement Thing behavior
Interaction Model
JSON-LD representation format to describe Thing instances with metadata. Uses formal interaction model and domain-specific vocabularies to uniformly describe Things, their capabilities, and how to use them.
WoT Thing Description (TD)
Capture how the formal Interaction Model is mapped to concrete protocol operations (e.g., CoAP) and platform features (e.g., OCF). The templates are done once per ecosystem and require a vocabulary for each base protocol (e.g., HTTP in RDF).
WoT Binding Templates
…
HTTP
MQTT
CoAP
TD
Events
Properties
Actions
An index.html
for Things
Protocol Bindings

## Slide 22: Describe Existing IoT Ecosystems
Any IoT Device
Data Model
Interaction Model
JSON-LD representation format to describe Thing instances with metadata. Uses formal interaction model and domain-specific vocabularies to uniformly describe Things, their capabilities, and how to use them.
WoT Thing Description (TD)
Common JavaScript object API for an IoT runtime system similar to the Web browser. Enable portable scripts that implement the behavior of Things and Consume across different vendors, devices, and environments.
Behavior must also be identifiable through domain-specific vocabulary terms.
WoT Scripting API
Common Runtime
Behavior
Application Script
Capture how the formal Interaction Model is mapped to concrete protocol operations (e.g., CoAP) and platform features (e.g., OCF). The templates are done once per ecosystem and require a vocabulary for each base protocol (e.g., HTTP in RDF).
WoT Binding Templates
…
HTTP
MQTT
CoAP
TD
Events
Properties
Actions
An index.html
for Things
Protocol Bindings

## Slide 23: Describe Existing IoT Ecosystems
Any IoT Device
Data Model
Interaction Model
JSON-LD representation format to describe Thing instances with metadata. Uses formal interaction model and domain-specific vocabularies to uniformly describe Things, their capabilities, and how to use them.
WoT Thing Description (TD)
Common JavaScript object API for an IoT runtime system similar to the Web browser. Enable portable scripts that implement the behavior of Things and Consume across different vendors, devices, and environments.
Behavior must also be identifiable through domain-specific vocabulary terms.
WoT Scripting API
Common Runtime
Behavior
Application Script
Capture how the formal Interaction Model is mapped to concrete protocol operations (e.g., CoAP) and platform features (e.g., OCF). The templates are done once per ecosystem and require a vocabulary for each base protocol (e.g., HTTP in RDF).
WoT Binding Templates
…
HTTP
MQTT
CoAP
TD
Events
Properties
Actions
An index.html
for Things
Protocol Bindings
WoT Security and Privacy metadata and guidelines for existing security (e.g., IETF ACE)

## Slide 24: W3C WoT Architecture
Direct Thing-to-Thing
Interaction
Existing Device
Complement Existing Devices
+
Thing
⇒
Edge
Cloud
Seamless
Web Integration
Optional
Remote Access and Synchronization
WoT Servient
Behavior
Affordances
Protocol Bindings
Security Configuration
WoT Servient
Behavior
Affordances
Protocol Bindings
Security Configuration
Thing
Behavior
Affordances
Protocol Binding
Security Configuration
Thing + Consumer
Behavior
Affordances
Protocol Bindings
Security Configuration
Protocol
Consumer
Behavior
Protocol Bindings
Security Configuration
Local Network
Thing-to-Cloud
Thing-to-Gateway
Data Schemas
Data Schemas
Data Schemas
Data Schemas
= Thing Description (TD)

## Slide 27: W3C WoT Thing Description
{
"@context": [
"https://www.w3.org/2019/wot/td/v1",
{ "cov": "http://proto.example.org/coap-binding#",
"iot": "http://schema.example.org/" }
],
"@type": ["Thing"],
"id": "urn:dev:ops:32473-WoTLamp-1234",
"title": "MyLEDThing",
"securityDefinitions": {
"default": { "scheme": "bearer" },
"dtls": { "scheme": "psk" }
},
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"description": "Sets the brightness between 0 and 100%",
"type": "integer",
"minimum": 0,
"maximum": 100,
"iot:Unit": "iot:Percent", "forms": [ ... ]
}
},
"actions": {
"fadeIn": {
JSON-LD 1.1 (Linked Data)
Extensions and domain-specific vocabulary
JSON Schema
vocabulary as Linked Data
W3C WoT TD vocabulary
Protocol
Bindings
Security Metadata
User-defined values

## Slide 28: W3C WoT Thing Description
...
"actions": {
"fadeIn": {
...
"forms": [
{ /// TD defaults: POST to invoke Action
"href": "https://myled.example.com:8080/fadein",
"mediaType": "application/json"
},
{
"href": "coaps://myled.example.com:5684/on",
"mediaType": "application/ocf+cbor",
"cov:methodCode": 3, /// PUT instead of POST to invoke
"cov:options": [{
"cov:optionNumber": 2053, /// OCF-Content-Format-Version
"cov:optionValue": "1.1.0"
}]
}
]
},
"fadeOut": {
...
"forms": [
{
"href": "https://myled.example.com:8080/fadeout",
"mediaType": "application/json"
Basics to build the request
Deviation from defaults
Like with HTML forms, the server/Thnig can tell the client/Consumer how to create a request

## Slide 29: Combining Existing Standards
Data Schemas
Hyper-media
Semantic Annotations
TD
JSON Schema
Description of existing data formats
Validation of payloads through available implementations
Already in use by industry, e.g., OpenAPI (microservices), Open Connectivity Foundation

## Slide 30: Combining Existing Standards
Data Schemas
Hyper-media
Semantic Annotations
TD
JSON Schema
Description of existing data formats
Validation of payloads through available implementations
Already in use by industry, e.g., OpenAPI (microservices), Open Connectivity Foundation
JSON-LD 1.1
Semantic meaning through controlled vocabularies enables interoperability
Reasoning through ontologies makes TDs machine-understandable
Knowledge Graphs interlink TDs with all related information

## Slide 31: Combining Existing Standards
Data Schemas
Hyper-media
Semantic Annotations
TD
JSON Schema
Description of existing data formats
Validation of payloads through available implementations
Already in use by industry, e.g., OpenAPI (microservices), Open Connectivity Foundation
JSON-LD 1.1
Semantic meaning through controlled vocabularies enables interoperability
Reasoning through ontologies makes TDs machine-understandable
Knowledge Graphs interlink TDs with all related information
Web Links and Forms
Uniform REST interface describes how to interact given an IoT protocol such as HTTP and CoAP, but also MQTT, Modbus, UA Binary, etc.
URIs encode the IoT protocol and
target address in a simple string
Media Types identify the payload format (e.g., application/json)

## Slide 32: node-wot: Build Your Own Web of Things
node-wot Servient
node-wot Servient
Protocol Bindings
Consumer Script
HTTP(S)
MQTT
CoAP(S)
...
Protocol Bindings
System API
Local Hardware
Security Metadata
Thing Script
HTTP(S)
MQTT
CoAP(S)
...
WoT Runtime
Scripting API
WoT Runtime
Scripting API
Proprietary Communi- cation
Legacy Device
TD
TD
TD

## Slide 33: Eclipse Thingweb: node-wot & more
https://github.com/eclipse/thingweb.node-wot/
https://www.thingweb.io/
https://projects.eclipse.org/projects/iot.thingweb

## Slide 34: Spirit of the Present: Semantic Interoperability
Independent digitalization led to various siloed ecosystems
  Custom protocols and data models form implicit interaction models
  High integration costs to access and harmonize data
  Documentation usually for human readers only
W3C WoT aims at breaking up the silos for interoperability in the IoT and at making interactions and data machine-understandable through semantic annotations

## Slide 35: The Spirits of Web of Things
Past
Web Presences
Putting Things to REST
Constrained RESTful Environments
Yet to Come
More Bindings
More Semantics
Better Actions
Present
W3C Standardization
Thing Description
node-wot

## Slide 36: Industrial Protocol Bindings

## Slide 37: Industrial IoT Ecosystems
BACnet
Building automation
Protocol with object-based information model
Modbus
Energy systems, supervisory logic
Simple protocol for addressing registers

## Slide 38: Industrial IoT Ecosystems
OPC Unified Automation (UA)
Factory and process automation
Graph-based information model and communication protocols
 For management/monitoring
OPC UA Field-Level Communications (FLC)
Extension to cover field controllers and devices
Integrates TSN, which is configured via NETCONF
 For real-time applications

## Slide 39: OPC UA Binding
Mapping to Properties, Actions, and Events (with opc:methodName field in from)
  Variable nodes  Properties
  Method nodes  Actions (node attributes become TD fields)
  Node alerts  Events
DataSchema
  OPC UA uses binary data types, hence JSON Schema must be further annotated
  Would be binding-specific, ergo form field, but form metadata not available to ContentSerdes
  opc:dataType annotation in DataSchema
Form href URI (UA-Binary over TCP)
  Adopt opc.tcp schema, but extend with ;-separated query similar to OPC UA tooling
  opc.tcp://localhost:5050/server-path?ns=1;s=mynode
Form contentType
  UA-Binary has no registered mediatype (similar to URI schema, needs a push within OPCF)
  application/x.opcua
Sciullo, Bhattacharjee, Matthias Kovatsch. “Bringing Deterministic Industrial Networking to the W3C Web of Things with TSN and OPC UA.” Proc. IoT 2020. Malmö, Sweden. Sep 2020

## Slide 40: NETCONF Binding
Mapping to Properties, Actions, and Events (built on RESTCONF)
  Leaf-nodes  Properties
  RPCs  Actions
  Notifications  Events
DataSchema
  Mostly works, as YANG is XML-based
  Must add mechanism for XML node attributes (e.g., )
  nc:container and nc:attribute annotations – should become general XML mechanism
Form href URI (XML messages over SSH transport)
  Similar to RESTCONF URIs, but with support for datastores (RESTCONF has implicit rules)
  netconf://localhost:830/running/ietf-interfaces:interfaces/interface=eth0/type
Form contentType
  Re-usable from RESTCONF
  application/yang-data+xml
Sciullo, Bhattacharjee, Matthias Kovatsch. “Bringing Deterministic Industrial Networking to the W3C Web of Things with TSN and OPC UA.” Proc. IoT 2020. Malmö, Sweden. Sep 2020

## Slide 41: Examples
OPC UA
"properties": {
"Velocity": {
"type": "number",
"observable": true,
"opc:dataType": "Double",
"forms": [{
"href": "opc.tcp://xts.local:5050/ns=1;\\ s=GVL.OPC_Interface.MOVER[1].Input.Velocity",
"contentType": "application/x.opcua-binary" }] },
... },
"actions": {
"Execute": {
"input": {
"type": "boolean", "opc:dataType": "Boolean" },
"output": {
"type": "boolean", "opc:dataType": "Boolean" },
"forms": [{
"href": "opc.tcp://xts.local:5050/ns=1;\\
s=GVL.OPC_Interface.XTS.Input.Execute",
"contentType": "application/x.opcua-binary",
"opc:method": "Call" }] } }
NETCONF
"properties": {
"admin-control-list": {
"type": "array",
"items": {
"type": "object",
"properties": {
"index": {
"type": "number", "minimum": 0, "maximum": 127 },
"time-interval": {
"type": "number", "minimum": 0, "maximum": 4294967295 },
"gate-state": {
"type": "number", "minimum": 0, "maximum": 255 } } },
"uriVariables": {
"datastore": {
"@type": "nc:Target",
"type": "string",
"enum": ["candidate", "running", "startup"] },
"interface": {
"type": "integer", "minimum": 0, "maximum": 7 } },
"forms": [{
"href": "netconf://172.17.0.2:830/{datastore}/huawei:tsn-configuration\\ /interface={datastore}/gate-parameters/admin-control-list",
"contentType": "application/yang-data+xml",
"nc:curies": { "ht": "urn:ietf:params:xml:ns:yang:huawei-tsn" } }] },
...

## Slide 42: From TDs to Knowledge Graphs

## Slide 43: WoT Thing Description Is a Framework
Provisioning of domain-specific vocabularies and ontologies
  schema.org IoT Extension
    W3C Community Group
  Bridging existing ontologies, e.g.,
    SSN
    eCl@ss
    Building Topology Ontology
  Converting existing models, e.g.,
    OPC UA Companion Specifications
    OneDM (ZigBee Cluster Lib etc.)
schema:thing
IotCapability
InteractionPattern
IotAction
IotEvent
IotProperty
acceptsInputData
providesOutputData
providesInteractionPattern
IotDataItem
schema:PropertyValue
schema:PropertyValueSpec.
IotThing
hasIotThing
hasIotCapability

## Slide 44: WoT Thing Description Is a Framework
Management of TD information
  Thing Directory to be standardized
    Registration
    Lookup
  TDs are Linked Data (JSON-LD 1.1)
    Thing Directory is a knowledge base
    Enrich with any data, e.g., maintenance
    Serialize context-aware TDs, e.g., for admin
  TDs is a modern version of the I4.0 Asset Administration Shell
    Describes the interface
    Can store lifetime data
    Has no baggage of executable code
TD
TD
“JSON-LD Framing”
Semantic query
TD
TD

## Slide 45: Hypermedia-driven Actions

## Slide 46: Actions in Thing Descriptions
...
"actions": {
"fadeIn": {
...
},
"fadeOut": {
...
},
"toggle": {
...
},
"execute": {
...
}
},
...
All examples just show simple Actions that can be completed in a single step
This has been sufficient for most use cases considered so far
Often there is the implicit assumption that a Consumer needs to know in what order to interact with the different affordances to follow a process

## Slide 47: What if only the Thing Knows the Process?
Electric Vehicle Charging
Robots (PLCopen)

## Slide 48: Let Machines use Things Like We Browse the Web
Thing A
Follow links
Client
Auth-Server
Dynamically extend process flow
Resource Directory
Entry URI
Submit forms
Action Result
Thing B
Thing C
Thing D
Choice &
redundancy

## Slide 49: Spirit of Yet to Come: Up to You!
AI for Industry 4.0 requires industrial protocol bindings for W3C WoT
W3C WoT only defines the framework and still requires WoT-oriented vocabularies and ontologies as JSON-LD context extension files  Industrial Knowledge Graphs can help
W3C WoT currently only describes simple, single-step interactions, so that complex workflows and processes still need manual programming  Action responses with affordances and Hypermedia Agents can help

## Slide 50: Contact
Dr. Matthias Kovatsch
Principal Researcher
Huawei, Munich Research Center
matthias.kovatsch@huawei.com
(Note that this is a research view)